## Slide 1: LDdriver V9.0: Tapes in disguise OpenVMS Advanced Technical Bootcamp May 2007
Jur van der Burg
digiater.nl
Notes: Presentation Title
<number>

## Slide 2: LDdriver: What can it do?
July 30, 2026
<number>
Use a file on any disk as a disk
Use a file on any disk as a tape
Use a range of logical blocks on a disk as a new disk
Investigate I/O behavior
Test application error handling
Play around with disks or tapes without doing damage
Create havoc (with privileges)
Notes: Presentation Title
<number>

## Slide 3: Where can I find it?
July 30, 2026
<number>
On the main LDdriver site
http://www.digiater.nl/lddriver
http://www.digiater.nl/downloads
  LD V8.3 will remain available as it is the last release that supports VAX
On the OpenVMS freeware website
  This may not be the latest version
  http://www.hp.com/go/openvms/freeware
Notes: Presentation Title
<number>

## Slide 4: Basics
July 30, 2026
<number>
Use a file as a disk
Create a file on a physical disk:
  LD CREATE DKA100:[LD]DISK/SIZE=10000
Connect the file to a device:
  LD CONNECT DKA100:[LD]DISK LDA1
Use it:
  INIT LDA1: LDDISK
  MOUNT LDA1: LDDISK
  .....
  DISMOUNT LDA1:
Disconnect the file:
  LD DISCONNECT LDA1
Notes: Presentation Title
<number>

## Slide 5: New features in V9.0
LD CREATE/ERASE
  Erases container file after creation
  Implicit when highwater marking is turned on
  Uses erase pattern set by $ERAPAT
  Warning message issued if file is more than 100000 blocks (VMS V8.2 and up)
    %LD-W-HIGHWATER, Highwater marking is enabled on device, be patient
  If combined with /EXTEND only the extended part will be erased
LD SHOW/SYMBOL
  Retrieves unit number and container filename in DCL symbols: LD_UNIT and LD_CONTAINER
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 6: New features in V9.0 - continued
LD SHOW/FULL
  Shows extended attributes of LD device
  $ ld show/all/full %LD-I-CONNECTED, Connected _$3$LDA1: to $1$DGA100:[JUR]FILE.DSK;1 -LD-I-OPTIONS, Shared %LD-I-CONNECTED, Connected _$3$LDA2: to _$3$DQA0: -LD-I-OPTIONS, Replaced, Trace active, No DSE support, Not Forced Error capable
LD SHOW/TRACE/TIMESTAMP=START or END
  Allows selection of absolute start and end time of trace data
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 7: New features in V9.0 - continued
LD CONNECT/LOGICAL=(NAME=logical-name[,TABLE=table][,MODE=mode])
  Setup a logical name associated with the connected LD device
  Privileges dictate modes and tables
LD SHOW/TRACE /LBN=[HEX,DECIMAL]
/BYTECOUNT=[HEX,DECIMAL]
  Alter data format in trace
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 8: New features in V9.0 - continued
Accurate timestamps in trace data
  Only in VMS V8.3 and up
  $ ld show/trace lda1
I/O trace for device $3$LDA1:
  17-MAY-2006 09:21:15.16 on node THEBAT
  End Time Elaps Pid Lbn Bytes Iosb Function
  ---------------------------------------------------------------------
  09:21:12.232269 00.000000 2060042F 0 0 NORMAL PACKACK
  09:21:12.240950 00.008581 2060042F 1 512 NORMAL READPBLK
  09:21:12.247513 00.006426 2060042F 1034 512 NORMAL READPBLK
  09:21:12.248595 00.000959 2060042F 50033 512 NORMAL READPBLK
  09:21:12.249557 00.000838 2060042F 50034 512 NORMAL READPBLK
Control utility rewritten in Ansi-C
  Allows much more checking by the compiler
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 9: Magtape support
Just use LM (Logical Magtape) instead of LD for most commands
Startup like LD:
  @SYS$STARTUP:LM$STARTUP
Minimum container file size is 5000 blocks
Container file has a private format
Volume switching support
No fastskip support
No density switching support
No compaction support
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 10: Container file creation
Use LM CREATE instead of LD CREATE
  This adds metadata to the container file
  Not needed for correct operation right now
    Will be needed in the future for fast skip
  Metadata can be initialized later on
    Original file contents will be preserved as the metadata space will always be reserved
    Initialize later on with LM CONNECT/INIT
  This will not be done by default as it would overwrite the first block of a file
    What if you would connect the wrong file by mistake?
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 11: Container file metadata
%LM-I-METADATA, Metadata available
Version: 1
Creator: JUR
Process name: SysDamager
Account: SYSTEM
UIC: [100,100]
Created on system: THEBAT
VMS version: V8.3
Time at creation: 8-MAY-2007 20:50:19.90
Time at last connect: 8-MAY-2007 20:50:25.49
Time at last disconnect: 8-MAY-2007 20:53:23.54
Data start: 1
Data size: 9999
Flags: tagsinuse
Checksum: A7C35A3F
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 12: Basic use
$ lm create tape.dsk/size=10000
$ lm connect/log tape.dsk lma1:
%LM-I-CONNECTED, Connected $3$LMA1: to $3$DKA100:[JUR.LD]TAPE.DSK;1
$ init lma1: test
$ backup sys$sysroot:[syshlp.examples.ld]*.* lma1:test/verify
%MOUNT-I-MOUNTED, TEST mounted on _$3$LMA1: (THEBAT)
%BACKUP-I-STARTVERIFY, starting verification pass at 17-MAY-2007 11:14:07.78
$ dismount lma1:
$ lm disconnect lma1:/log
%LM-I-DISCONNECTED, Disconnected $3$LMA1: from $3$DKA100:[JUR.LD]TAPE.DSK;1
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 13: Volume switching
Allows loading a new container file as soon as backup runs out of space
Manual load/unload
  LM UNLOAD LMA1
  LM LOAD NEWFILE.DSK LMA1
One step approach
  LM SWITCH NEWFILE.DSK LMA1
    This will automatically unload the old container file
Load existing file if the unit is unloaded (for example, $ DISMOUNT/UNLOAD)
  LM LOAD LMA1
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 14: Volume switching - continued
Tape will initially be loaded
$ lm connect tape lma1/full/log
%LM-I-CONNECTED, Connected $2$LMA1: to $2$DKA400:[JUR]TAPE.DSK;1
-LM-I-OPTIONS, Tape unit, Tape loaded
$ mount/for lma1
%MOUNT-I-MOUNTED, TEST mounted on _$2$LMA1: (THEBAT)
$ dismount lma1
$ lm show lma1/full
%LM-I-CONNECTED, Connected $2$LMA1: to $2$DKA400:[JUR]TAPE.DSK;1
-LM-I-OPTIONS, Tape unit, Tape unloaded
The behavior is just like a real tape unit
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 15: Volume switching - continued
It is possible to create a tape device without an attached container file
  $ lm connect lma2/noload/log/full
  %LM-W-NOTCONNECTED, Device $2$LMA2: is not connected
  -LM-I-OPTIONS, Not Forced Error capable, Tape unit, Tape unloaded
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 16: Tape data trace
Data to or from disk on behalf of the driver is not logged by default
This can be enabled with LM TRACE/ALL
It will show up in trace data with a PID field of zero
Disk requests are subject to segmentation dictated by the maximum transfer size of the physical disk driver
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 17: Tape data trace - continued
$ lm trace lma1/all
$ init lma1 test
$ mount lma1 test
%MOUNT-I-MOUNTED, TEST mounted on _$3$LMA1: (THEBAT)
$ lm show/trace lma1
I/O trace for device $3$LMA1:
8-MAY-2007 20:51:59.14 on node THEBAT
End Time Elaps Pid Lbn Bytes Iosb Function
---------------------------------------------------------------------
20:51:49.649071 00.000005 2020042F 0 0 NORMAL PACKACK
20:51:49.649133 00.000000 2020042F 0 0 NORMAL REWIND
20:51:49.649174 00.000001 2020042F 0 0 NORMAL SETMODE|MT3_DENSITY
20:51:49.664598 00.014676 00000000 1 131072 NORMAL READPBLK
20:51:49.666553 00.001917 00000000 257 131072 NORMAL READPBLK
20:51:49.676429 00.009853 00000000 513 131072 NORMAL READPBLK
20:51:49.686808 00.010357 00000000 769 131072 NORMAL READPBLK
20:51:49.686837 00.036922 2020042F 0 80 OPINCOMPL READPBLK
20:51:49.686904 00.000001 2020042F 0 0 NORMAL REWIND
20:51:49.686945 00.000000 2020042F 0 0 NORMAL SETMODE|MT3_DENSITY
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 18: Diagnostics
LM ANALYZE file.dsk [/RECORDS] [/DATA]
  Will detect container file issues
  Normally not needed by end user
    $ lm analyze tape
    %LM-I-METADATA, Metadata available
    Version: 1
    Creator: JUR
    Process name: Jur van der BUG
    Account:
    UIC: [100,100]
    Created on system: THEBAT
    VMS version: V8.3
    Time at creation: 15-MAY-2007 20:13:21.30
    Time at last connect: 15-MAY-2007 20:50:13.27
    Time at last disconnect: 15-MAY-2007 20:50:26.74
    Data start: 1
    Data size: 99999
    Flags: tagsinuse
    Checksum: C26E5931
    %LM-I-ANALYZEOK, Container file structure successfully verified
    Bytes read: 49283072
    Records read: 5967
    Databytes read: 48800144
    Eof count: 4
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 19: Container file layout
For disk it’s easy: ODS2 or ODS5
For tape it’s a private format
  Header record layout
TAG longword unsigned;
RECNUM quadword unsigned;
OFFSET quadword unsigned;
BCNT longword unsigned;
FLAGS structure longword unsigned;
DATA address;
  Trailer record layout
BCNT longword unsigned;
TAG longword unsigned;
Bytecount in trailer record facilitates reverse skip
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 20: Driver internals
The big issue: writing sequential variable records to a block structured medium
Internal buffering required for efficiency
Buffer management is complex
The buffer manager is a sort of ‘Kernel mode RMS’
  Must be able to seek to any position
All manipulation must be done from system context
  No usermode or process available
Data copies needed from/to user buffer to driver buffer by double mapping
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 21: Driver internals - continued
Internal buffer is fixed 512Kb
  Allocated from nonpaged pool for every unit
The most efficient way to handle data
One driver for LD and LM devices!
  Driver is still named SYS$LDDRIVER.EXE
  The device name during driver connect will determine if it’s a disk or a tape
  Easy driver maintenance (one source file)
  If an old LDdriver is active when installing LD V9.0 then LM can not be used before the system has been rebooted
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 22: Restrictions
July 30, 2026
<number>
LM devices can not be shared
End of data is currently fixed at 95% of the container file size
Non-foreign (Files-11) mounted tapes may not handle certain files
  VMS I/O subsystem enforces a minimum record size of 14 bytes for tape
  Copying .OBJ files or other types may give SS$_BADATTRIB errors
  Real tape devices behave the same
Notes: Presentation Title
<number>

## Slide 23: Restrictions - continued
July 30, 2026
<number>
Watchpoints are not supported on virtual tapes
LD V8.3 is the last release supporting VAX
  Too much 64-bit stuff needed
  Limited interest in new features
Notes: Presentation Title
<number>

## Slide 24: Known problems
Switching volumes on Files-11 mounted tape may give errors
LM SHOW/TRACE/CONTINUOUS may cause invalid data to be written to tape
Accurate timing in trace data may we way off if a cpu has been stopped and restarted
  Workaround is to disconnect and reconnect the LM or LD device
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 25: Limits
July 30, 2026
<number>
Create as many devices as your diskspace allows
Creation of any device takes BYTLM quota from the creating process
The tracebuffer as well as watchpoints come out of non-paged pool and are charged against BYTLM as well
If 9999 LD devices are not enough then you can create LD devices on other controllers, like LDB1:, LDC1:, etc.
Configure the driver with @SYS$STARTUP:LD$STARTUP x where x is the controller to use.
Notes: Presentation Title
<number>

## Slide 26: Old versions
July 30, 2026
<number>
LD V8.3:
  LD V8.3 has no new features when compared to V8.2
  It is only a bug fix release (and what a bug!).
    If a container file resides on a volumeset then reads and writes are always directed to the member of the set where the first blocks of the file are located
    So if data would need to go to another member it would go to this member
    Guess what the result will be
    Fix is present in V9.0
    Problem was introduced in LD V8.0, on Alpha, IA64 and VAX, and is also present in LD V8.1 and LD V8.2
    Native version of LD in VMS V8.2 is not affected
    Native version of LD in VMS V8.3 is affected
    Next VMS release after VMS V8.3 will have the fix
Notes: Presentation Title
<number>

## Slide 27: Futures
Automatic volume switch support
  LM AUTOSWITCH file1,file2,… LMAx
  Imitates a stacker
  Mechanism to automatically create new container files
Fast skip support
  Already partly implemented but not finished in V9.0
Density select
  Might be limited in use
Callback to applications on certain driver conditions (via AST’s)
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 28: Futures - continued
Compaction may be possible now that we can handle variable length records
  This might be used for Logical Disks as well (data compression on virtual disks!)
You name it
  Money might speed up things considerably 
July 30, 2026
<number>
Notes: Presentation Title
<number>

## Slide 29: More information
July 30, 2026
<number>
After installation: $ LD HELP
LDdriver website:
  http://www.digiater.nl/lddriver
  http://www.digiater.nl/downloads
  LDdriver article from the HP technical journal
  Old presentations
Questions / Bugs / Ideas?
  Email: lddriver@digiater.nl
Notes: Presentation Title
<number>

## Slide 30
Notes: Presentation Title
<number>

## Slide 31: LD_FILE.COM
July 30, 2026
<number>
$ ld create disk1.dsk /size=5000
$ ld connect disk1.dsk lda1:
$ ld show lda1:
$ ld trace lda1:
$ init lda1: test
$ mount lda1: test
$ dir lda1:[000000]
$ ld show/trace lda1:
$ ld trace/reset lda1:
$ dismount lda1:
$ ld show/trace lda1:
$ ld disconnect lda1:
$ delete disk1.dsk;
Notes: Presentation Title
<number>

## Slide 32: LD_FILE_SHARE.COM
July 30, 2026
<number>
$ if f$search("disk1.dsk") .eqs. ""
$ then
$ ld create disk1.dsk /size=5000
$ ld connect disk1.dsk lda1:/share/alloclass=4/log
$ init lda1: test
$ else
$ ld connect disk1.dsk lda1:/share/alloclass=4/log
$ endif
$ mount/system lda1: test
$ show dev lda1
$ inquire dummy "return to continue"
$ dismount lda1:
$ ld disconnect/log lda1:
$ if f$search("disk1.dsk") .nes. "" then delete disk1.dsk;
Notes: Presentation Title
<number>

## Slide 33: LD_FILE_SHARE_LOCK.COM
July 30, 2026
<number>
$ if f$search("disk1.dsk") .eqs. ""
$ then
$ ld create disk1.dsk /size=5000
$ ld connect disk1.dsk lda1:/share/alloclass=4/log/lock
$ init lda1: test
$ else
$ ld connect disk1.dsk lda1:/share/alloclass=4/log/lock
$ endif
$ mount/system lda1: test
$ show dev lda1
$ inquire dummy "return to continue"
$ dismount lda1:
$ ld disconnect/log lda1:
$ if f$search("disk1.dsk") .nes. "" then delete disk1.dsk;
Notes: Presentation Title
<number>

## Slide 34: LD_FILE_TRACE.COM
July 30, 2026
<number>
$ on control_y then goto exit
$ ld create disk1.dsk /size=5000
$ ld connect disk1.dsk lda1:/log
$ init lda1: test
$ mount lda1: test
$ ld trace lda1:
$loop:
$ dir lda1:[000000]
$ wait 0:0:5
$ analyze/disk lda1:
$ wait 0:0:5
$ goto loop
$ dismount lda1:
$exit:
$ set noon
$ dismount lda1:
$ ld trace/stop lda1:
$ ld disconnect lda1:
$ delete disk1.dsk;
Notes: Presentation Title
<number>

## Slide 35: LD_FILE_SHADOW.COM
July 30, 2026
<number>
$ ld create disk1.dsk /size=5000
$ ld create disk2.dsk /size=5000
$ ld connect disk1.dsk lda1:/log/alloclass=4
$ ld connect disk2.dsk lda2:/log/alloclass=4
$ ld trace lda1:
$ ld trace lda2:
$ init lda1: test
$ mount dsa0:/shadow=($4$lda1:,$4$lda2:) test
$ ld show/trace lda1:
$ ld show/trace lda2:
$ ld trace/reset lda1:
$ ld trace/reset lda2:
$ show shadow/copy
$ inquire dummy "return to continue"
$ dismount dsa0:
$ ld show/trace lda1:
$ ld show/trace lda2:
$ ld disconnect lda1:
$ ld disconnect lda2:
$ delete disk1.dsk;
$ delete disk2.dsk;
Notes: Presentation Title
<number>

## Slide 36: LD_LBN.COM
July 30, 2026
<number>
$ phdev := $9$dka400:
$ show dev 'phdev'
$ ld connect 'phdev' lda1:/log/lbn=(start=0,count=10000)
$ ld connect 'phdev' lda2:/log/lbn=(start=10000,count=10000)
$ ld connect 'phdev' lda3:/log/lbn=(start=20000,count=10000)
$ ld connect 'phdev' lda4:/log/lbn=(start=30000,count=10000)
$ init lda1: test1
$ init lda2: test2
$ init lda3: test3
$ init lda4: test4
$ mount lda1: test1
$ mount lda2: test2
$ mount lda3: test3
$ mount lda4: test4
$ show dev lda1
$ show dev lda2
$ show dev lda3
$ show dev lda4
$ show dev 'phdev'
$ inquire dummy "return to continue"
$ dismount lda1:
$ dismount lda2:
$ dismount lda3:
$ dismount lda4:
$ ld disconnect/log/all
$ show dev 'phdev'
Notes: Presentation Title
<number>

## Slide 37: LD_LBN_SHARE.COM
July 30, 2026
<number>
$ phdev := $9$dka400:
$ show dev 'phdev'
$ ld connect 'phdev' lda1:/log/lbn=(start=0,count=10000)/share/alloclass=4
$ ld connect 'phdev' lda2:/log/lbn=(start=10000,count=10000)/share/alloclass=4
$ ld connect 'phdev' lda3:/log/lbn=(start=20000,count=10000)/share/alloclass=4
$ ld connect 'phdev' lda4:/log/lbn=(start=30000,count=10000)/share/alloclass=4
$ mount/system lda1: test1
$ mount/system lda2: test2
$ mount/system lda3: test3
$ mount/system lda4: test4
$ show dev lda1
$ show dev lda2
$ show dev lda3
$ show dev lda4
$ show dev 'phdev'
$ inquire dummy "return to continue"
$ dismount lda1:
$ dismount lda2:
$ dismount lda3:
$ dismount lda4:
$ ld disconnect/log/all
$ show dev 'phdev'
Notes: Presentation Title
<number>

## Slide 38: LD_REPLACE.COM
July 30, 2026
<number>
$ phdev := $9$dka400:
$ show dev 'phdev'
$ ld connect 'phdev' lda1:/log/replace
$ ld trace lda1:
$ init lda1: test1
$ mount lda1: test1
$ show dev/full lda1
$ show dev/full 'phdev'
$ ld show/trace lda1:
$ inquire dummy "return to continue"
$ dismount lda1:
$ ld disconnect/log lda1:
$ show dev 'phdev'
Notes: Presentation Title
<number>

## Slide 39: LD_MOUNTVER.COM
July 30, 2026
<number>
$ ld create disk1.dsk
$ ld connect/log/symbol disk1.dsk
$ init/nohigh/system lda'ld_unit': test
$ mount lda'ld_unit': test
$ ld trace lda'ld_unit':
$ ld watch lda'ld_unit': 1/action=error=%x84/function=code=%x0808
$ ld watch lda'ld_unit': 10/action=error=%x84/function=read
$ ld watch lda'ld_unit': 10/action=opcom/function=read
$ ld show/watch lda'ld_unit':
$ reply/enable/temp
$ spawn/nowait/input=nl: dump lda'ld_unit':/block=(start=10,count=1)
$ inquire dummy "return to continue"
$ ld nowatch lda'ld_unit':
$ ld show/trace lda'ld_unit':
$ reply/disable
$ wait 0:0:1
$ dism lda'ld_unit':
$ set noon
$ ld trace/stop lda'ld_unit':
$ ld disc lda'ld_unit':
$ delete/nolog/noconf disk1.dsk;
Notes: Presentation Title
<number>

## Slide 40: LM_FILE.COM
$ lm create tape1.dsk /size=5000
$ lm connect tape1.dsk lma1:
$ lm show lma1:/full
$ lm trace lma1:/all
$ init lma1: test
$ mount lma1:/for
$ backup/log/verify sys$sysroot:[syshlp.examples.ld]*.* lma1:test
$ lm show/trace lma1:
$ lm trace/reset lma1:
$ dismount lma1:
$ lm show/trace lma1:
$ lm disconnect lma1:
$ lm analyze tape1.dsk
$ delete tape1.dsk;
July 30, 2026
<number>
Notes: Presentation Title
<number>