## Slide 1: Alpha 21364: A Scalable Single-chip SMP
Peter Bannon
Senior Consulting Engineer
Compaq Computer Corporation
Shrewsbury, MA
Notes: Thank you Lindley
It’s a pleasure to have a opportunity to talk about Alpha and the 21364 in particular.

## Slide 2: Outline
Alpha .vs. IA-64
Alpha Roadmap
Alpha 21164PC Update
Alpha 21264 Update
Alpha 21364
Conclusion
Notes: Today I would like to spend some time comparing Alpha and its design philosophy against IA-64.
I’ll then give a quick overview of the Alpha roadmap to position our current and future processors.
After an update on the 21164PC family, I’ll review the current status of the 21264 and try to provide some motivation for the 21364 design.
The bulk of the time will be spend reviewing the design of the 21364.
Lastly, I’ll have some conclusions.

## Slide 3: IA-64 .vs. Alpha Philosophy
EPIC
Smart compiler and a dumb machine
Compiler creates record of execution
Machine plays record
  Stall when compiler is wrong
Focus on vector programs
  Compiler transform scalar to vector
What about:
  function calls, indirection
  dynamic linking
  C++, Java/JIT
ALPHA
Smart compiler, smart machine, and a GREAT circuit design
Compiler creates record of execution
Machine exploits additional information available at runtime
  Works across barriers to compile-time analysis
Focus on scalar programs
  Add resources for vector
  Amdahl’s law
Notes: Looked at VLIW in 93&94, rejected for four reasons
1. VLIW did not fundamentally remove a difficult part of the hardware design.
2. Many of the compiler techniques associated with VLIW can also be applied to RISC machines
3. There are many road blocks to full analysis of a program by the compiler: function calls outside the compilation, indirection, dynamic linking
4. There is more to learn at runtime. We should not ignore this.
Alpha uses smart compilers, smart hardware and Great circuit design to build the fastest machine possible with a focus on scalar performance. Resources are added where needed to support vector program. Amdahl’s law assures us that this is the correct approach; you must have a fast scalar machine to have a fast vector machine.
Lets look at a familiar example.
Last year Intel began to introduce the IA-64 architecture. IA-64 was positioned as building on the best ideas of RISC and VLIW.
Both RISC and VLIW focus on pushing difficult or infrequent operations out of the hardware and into the compiler. Doing this requires a smart compiler and allows for a dump machine design. In a classic VLIW design the compiler schedules the code with full knowledge of the machine architecture. The hardware executes the instructions exactly the way the compiler planned, stalling or even breaking when the compiler is wrong.
The compiler can do a good job when it is provided with accurate profiling data that can be used to create the correct static schedule. For example, vector programs often behave this way.
However, large modern programs inhibit the compilers ability to determine the correct static schedule. Functions call out of a basic block or outside the compilation unit block optimizations. Call to shared libraries, DLL for example, also prevent optimization. Use of indirection to reference both data and code also reduces the compilers ability to find instruction level parallelism.
Alpha uses smart compilers, smart machines and GREAT circuit design to produce the highest level of performance.
The compiler schedules groups of instructions much like a VLIW compiler would, taking advantage of profiling data, prefetching, speculation, and predication.
The processor then uses additional information at runtime to expose additional parallelism as the program executes.
As the software world become more complex and dynamic, we believe that Alphas focus on scalar performance along with providing the necessary resources for vector like program will produce the best performance.

## Slide 4: Predication & Speculation
If ((b[j]==true) && (a[I+j]==true) && (c[I-j+7]==true))
IA-64 Alpha
1 R1=&b[j] 1 R1=&b[j]
R3=&a[I+j] R3=&a[I+j]
R5=&c[I-j+7] R5=&c[I=j+7]
2 ld R2=[R1] 2 ld R2=[R1]
ld.s R4=[R3] ld R4=[R3]
ld.s R6=[R5] ld R6=[R5]
4 P1,P2<-cmp(R2==true) 4 cmoveq r4, r31, r2
5 <P1> chk.s R4 5 cmoveq r6, r31, r2
<P1> P3,P4<-cmp(R4==true) 6 beq r2, else
6 <P3> chks R6
<P3> P5,P6<-cmp(R6==true)
7 <P5> br then
Notes: Compare the code for IA-64, presented last year with the output form toadies Unix compiler.
Alpha is already doing speculation of loads and predication with CMOV
The code on the left was copied from last years IA-64 presentation.
The code on the right was created by the currently shipping Unix compiler for Alpha. Note the use of speculative loads to improve the parallelism in the memory system, as well conditional move instructions to remove data dependent branches.
Assuming lots of functional units with 1 cycle operates and 2 cycle loads, both sequences execute in a similar number of architectural cycles.

## Slide 5: Predication & Speculation
If ((b[j]==true) && (a[I+j]==true) && (c[I-j+7]==true))
IA-64 Alpha
Instructions 12 9
Bytes 64 36
Branches 1 1
Mispredicts 16% 13% (measured)
Cycles 71 if () 6 dependent cycles if()
11 static full loop
6 executing on 21264
1 J Crawford, J Huck “Next Generation Instruction Set Architecture”, Microprocessor Forum 1997, pg 25
Notes: The increased size of the IA-64 instructions results in a larger memory foot print, allowing us to call Alpha a bit efficient architecture:).
Both code sequences contain a single branch, Intel reported a 16% mispredict rate for some design. We have measured 13% on the 21264.
I would now like to move away from architecture to actual implementations.
On the 21264, the static schedule for the FULL loop requires 11 cycles. However the out-or-order hardware allows the machine execute loop in 6 cycles.

## Slide 6: Queens on 21264
Several loops executing on the 21264
loop
LDL
CMOV
loop
loop
loop
loop
loop
loop
loop
loop
loop
loop
loop
LDA
LDA
LDA
LDA
LDA
LDA
LDL
LDL
LDL
LDL
LDL
CMOV
CMOV
CMOV
CMOV
CMOV
CMOV
CMOV
BEQ
BEQ
loop
LDL
CMOV
loop
loop
loop
loop
loop
loop
loop
loop
loop
loop
loop
LDA
LDA
LDA
LDA
LDA
LDA
LDL
LDL
LDL
LDL
LDL
CMOV
CMOV
CMOV
CMOV
CMOV
CMOV
CMOV
BEQ
BEQ
loop
LDL
CMOV
loop
loop
loop
loop
loop
loop
loop
loop
loop
loop
loop
LDA
LDA
LDA
LDA
LDA
LDA
LDL
LDL
LDL
LDL
LDL
CMOV
CMOV
CMOV
BEQ
LDL
loop
loop
loop
loop
loop
LDA
LDA
LDA
LDL
LDL
CMOV
loop
loop
loop
LDL
LDL
LDL
CMOV
CMOV
CMOV
CMOV
BEQ
CMOV
CMOV
BEQ
Fetch
Execute
Time
Notes: This slide show the execution of the full loop on the 21264.
The top group of blocks shows the instructions being fetched from the Icache and mapped into the issue queue. Each loop iteration is a different color. Note that fetching and mapping the instructions is the limiting work for this loop and that there is no bubble in the fetch stream for the taken branch.
The second group of blocks show the instructions executing. Note that the hardware is overlapping two iterations of the loop.
The CMOV instructions are broken into two parts by the mapper and execution stages because we are unwilling to map three source registers per cycle and likewise unwilling to add a third read port to the register file just for these instructions.
Next, I’d like to review the roadmap.

## Slide 7: Alpha Roadmap
1997
1998
1999
1995
1996
2000 2001
EV5/333 21164
EV6/575 21264
EV68/1000 21264
PCA56/533 21164PC
EV56/60021164
0.5m
0.35m
0.35m
0.35m
EV67/750 21264
0.28m
PCA57/600 21164PC
0.28m
0.18m
0.18m
Higher Performance
Lower Cost
...
EV8
0.13m
EV7/1000 21364
Notes: Next I would like to review the Alpha processor roadmap.
We will continue to introduce new cores at the high end and then cost reduce those products with improved technology and value engineering.
The 21164 is currently shipping in 0.35um at 600MHz. A cost reduced version of the part will be introduced this quarter in 0.28, also running at 600MHz.
The 21264 will begin shipping this quarter in 0.35. That part will be followed by shrinks into 0.28 and then 0.18 over the next 18 months.
The 21364 will be introduced in 0.18.
An entirely new core, EV8 will be introduced in 0.13.

## Slide 8: Alpha 21164PC
Shipping at 583MHz November 1998
  16.7/17.0 estimated SPECint95 (base/peak)
  20.7/22.7 estimated SPECfp95 (base/peak)
  340 MB/sec STREAMS
Chip features:
  1.0 cm2
  7 million transistors
  32K 2-set Icache
  16K virtual Dcache
  improved 3-cycle multiplier
  improved 6 bit/cycle divider
  increased write buffer size (8 x 32B)
  support for 200MHz off-chip cache
Notes: The 21164PC in 0.28um CMOS will be introduced later this quarter. At 583MHz, the part achieves 17 SPECint95 and 22.7 SPECfp95 using a 1MB external cache built form 200MHz PB2 SRAMs.
The 1cm die contains 7 million transistors. Several improvements were made to the parts compared to the original 0.35 version.
The Icache was doubled in size to 32K, and changed from direct mapped to 2-way set.
The Dcache was also doubled in size to 16KB and converted from a physically indexed, physically tagged cache to be virtually indexed and physically tagged.
A new integer multiplier is fully pipelined for 32 bit multiplies with a latency of 3 cycles.
A new floating point divider produces 6 result bits per cycle, compared to the 2.4 bit/cycle of the old design.
The floating point unit has improved support for IEEE floating point, including hardware support for NANs and infinity.
The size of the write buffer was increased and the chip now supports off-chip caches built from 200MHz PB2 SRAMS.

## Slide 9: Alpha 21264 Update
Microprocessor Forum 1996
  30+ SPECint95 and 50+ SPECfp95
  500MHz in 0.35um CMOS
  Spectacular memory bandwidth
  Systems 2H97
First power on July 1997 (no FP)
Full function power on Feb 1998
Production power on June 1998
Notes: At Microprocessor Forum in 1996, we introduced the architecture of the 21264. At that time we estimated a SPECint95 of 30 and a SPECfp95 performance of 50. In addition we hoped to ship systems by the end of 1997 at 500MHz. In the past we have taken great pride in delivering the performance we predict on time, this time we did not.
Completing the physical design and verification of the chip took considerably longer than we had planned. The first prototype version of the chip was powered on in the summer of 1997. The first full version of the chip was powered on in February of this year. System and software bring up had progressed rapidly, with the last version of the chip powering on in June. We now expect to ship systems later this quarter.
The current systems use 1/3rd speed caches while the simulated results used 2/3rd speed caches. This results in a 10% short fall on SPEC performance. During 1999, we expect to introduce systems with 2/3rd speed caches.

## Slide 10: Alpha 21264 Systems
AlphaServer 8400 with EV6/575
*37,541 tpmC at $79.4/tpmC for 8CPU 16GB
Sybase V11.9 available 12/98
**estimated
Notes: The AlphaServer 8400 is a large bus based SMP system. This chart shows the performance of the 21164 (ev5) as well as the 21264 (ev6) for 3 single processor benchmarks as well as 3 multiprocessor benchmarks.
Note that the 21264 is providing a 50% performance improvement over the 21164 using the same memory system.
Please note that the full TPC-C information is missing from your slides.
In the next slide I’d like to look more closely at the TPC performance

## Slide 11: Estimated time for TPC-C
New core
Higher MHz
Higher integration
Notes: This graph shows where a single processor is spending its time executing the TPC benchmark. Lower is faster.
The graph is normalized to the 21164 processor. For a single processor, simply replacing the 21164 with a 21264 results in doubling of performance. Since both chips where measured in the same memory system and at the same frequency, the improvement is completed attributed to the micro-architecture of the 21264. Note that significant improvement have been made in the compute, mispredict, cache and memory portions of the graph.
As the frequency of the chip is increased with improved technology in the coming years, the memory system will again dominate the performance of this application. This provides the motivation for the 21364 design.

## Slide 12: Alpha 21364 Goals
Improve
  Single processor performance, operating frequency, and memory system
  SMP scaling
  System performance density (computes/ft3)
  Reliability and availability
Decrease
  System cost
  System complexity
Notes: The 21364 processor will use a very high level of system integration to improve: single processor performance, SMP scaling, compute density, and reliability and availability. Naturally we would also like to reduce system cost and complexity.

## Slide 13: Alpha 21364 Features
Alpha 21264 core with enhancements
Integrated L2 Cache
Integrated memory controller
Integrated network interface
Support for lock-step operation to enable high-availability systems.
Notes: The 21364 will start with an enhanced version of the 21264 core. We will at an integrated L2 cache, Direct RAMbus memory controller, and a network interface. The chip will support lock-step operation to enable
high-availability systems.

## Slide 14: 21364 Chip Block Diagram
Memory
Controller
R
A
M
B
U
S
21264
Core
16 L1
Miss Buffers
L2
Cache
Address Out
Address In
Network
Interface
N
S
E
W I/O
16 L1
Victim Buf
16 L2
Victim Buf
64K Icache
64K Dcache
Notes: Here's a top level block diagram of the chip. The next few slides will provide additional detail.
We will start with core of the 21264. The number of outstanding cache block fills will be increased from 8 to 16. Misses to the L1 caches will first access the L2 cache. Data will be returned on a 128 byte wide bus.
References that miss the L2 cache will access the local memory and return data to the core. Memory locations not located in the local memory will access the network.
The integrated network interface will route the request to the appropriate node in the network using one of the 4 ports (N,S,E,W).
The 21164 cores 8 entry victim buffer is current used for both L1 and L2 victims. The new design will increase the size of the victim buffer to 16 x 64 byte blocks for L1->L2 victims. A new 16 x 64 bytes victim buffer will be used to hold victims leaving the L2 cache for the local memory or the network.

## Slide 15: 21364 Core
Int Reg
Map
Branch
Predictors
FETCH MAP QUEUE REG EXEC DCACHE
Stage: 0 1 2 3 4 5 6
L2 cache1.5MB
6-Set
Int Issue Queue
(20)
Exec
4 Instructions / cycle
Reg File
(80)
Victim Buffer
L1 Data
Cache
64KB
2-Set
FP Reg
Map
FP ADD
Div/Sqrt
FP MUL
Addr
80 in-flight instructions
plus 32 loads and 32 stores
Addr
Miss Address
Next-Line
Address
L1 Ins.
Cache
64KB
2-Set
Exec
Exec
Exec
Reg File
(80)
FP Issue Queue
(15)
Reg File
(72)
Notes: The 21364 will use the 21264 core. I’d like to briefly walk through the pipeline and then point out a few interesting features of the pipeline.
Four instructions are fetched from the 64K 2-set Icache each cycle and delivered to the integer and floating point mapers.
Following the path of integer instructions, the map stage maps the 32 virtual register numbers into the 80 physical register numbers which are then inserted into the issue queue.
Every cycle the integer issue queue will issue up to 4 instructions in age prioritized order, press out empty slots, and insert new instructions from the maper.
The next cycle the inputs are read from the register file.
Four integer units share two copies of the register file. The two lower units contain add and logic functions. These unit generate addresses for the cache system. Each of the upper units contains add, logic, shift, and branch functions. A fully pipelined integer multiply unit is part of one upper unit, while the other upper unit processes the population count and multi-media instructions.
The 64K 2-set L1 Dcache can process 2 loads or stores per cycle. References that miss are merged into cache block requests that access the L2 cache. Modified data is displaced during the fill and is buffered in a 16 entry victim buffer.

## Slide 16: Integrated L2 Cache
1.5 MB
6-way set associative
16 GB/s total read/write bandwidth
16 Victim buffers for L1 -> L2
16 Victim buffers for L2 -> Memory
ECC SECDED code
12ns load to use latency
Notes: The 1.5MB 6-set L2 cache has a 12 cycle load to use latency. This latency is set by the existing control in the core and is used to significantly reduce the power consumption of the L2 array.
The L2 cache and read or write 16 bytes/cycle at 1GHz, resulting in 16GB/second of read or write bandwidth.
The array is protected by a single error correct, double error detect ECC code. Error are corrected on the fly in hardware.

## Slide 17: Integrated Memory Controller
Direct RAMbus
  High data capacity per pin
  800 MHz operation
  30ns CAS latency pin to pin
6 GB/sec read or write bandwidth
100s of open pages
Directory based cache coherence
ECC SECDED
Notes: The chip contains a integrated Direct RAMbus memory controller. Direct RAMbus provides high data capacity per bin along with outstanding bandwidth and latency. The pin to pin delay for a page hit in the RDRAM is 30ns.
The memory controller will provide 6GB/sec of read or write bandwidth to the core. With 2GFLOPs, the chip provides 3byte/FLOP of usable memory bandwidth, a significant improvement over current systems.
To reduce memory latency the memory controller will track 100s of open pages in the RDRAM array.
A directory based cache coherence protocol is an integral part of the memory controller.
The memory is protected by a single error correct, double error detect ECC code.
EV56/600 300MB/sec / 1.2GFLOPS = 0.4 b/flop
EV6/600 1000MB/sec /1.2GFLOPS = 0.83b/flop

## Slide 18: Integrated Network Interface
Direct processor-to-processor interconnect
10 GB/second per processor
15ns processor-to-processor latency
Out-of-order network with adaptive routing
Asynchronous clocking between processors
3 GB/second I/O interface per processor
Notes: The integrated network interface allows multi-processor systems to be built using a 2D torus topology. Each node is capable of moving 10GB/second. Each hop in the network will take an average of 15ns.
The network moved data and control packets from the source to the destination. It does not garentee ordering. Adaptive routing of packets allows the network to detect and avoid hot spots.
Asynchronous clocking between processors removes the need to distribute a low skew clock within a large system.
A fifth port provides upto 3GB/sec on bandwidth to industry standard buses, PCI, PCI-X, AGP, and ServerNet to name a few.

## Slide 19: 21364 System Block Diagram
364
M
IO
364
M
IO
364
M
IO
364
M
IO
364
M
IO
364
M
IO
364
M
IO
364
M
IO
364
M
IO
364
M
IO
364
M
IO
364
M
IO
Notes: Here’s the block diagram of a 12 processor system using the 2D torus topology. Each processor may have its own local memory and may have its own local I/O connection. It is possible for a processor to operate in the system without memory or I/O if that is attractive

## Slide 20: Alpha 21364 Technology
0.18 m CMOS
1000+ MHz
100 Watts @ 1.5 volts
3.5 cm2
6 Layer Metal
100 million transistors
  8 million logic
  92 million RAM

## Slide 21: Alpha 21364 Status
70 SPECint95 (estimated)
120 SPECfp95 (estimated)
RTL model running
Tapeout 4Q99

## Slide 22: Conclusion
The 21364 integrated L2 cache and memory controller provide outstanding single processor performance
The 21364 integrated network interface enables high performance multi-processor systems
The high level of integration directly supports systems containing a large number of processors